## Slide 1: Considerations on Inter-DC Collective Communication Optimization(CCO)
IETF 120
Kehan Yao, China Mobile

## Slide 2
Collective Communications
Collective Broadcast()
Collective Gather()
Collective Allgather()
Collective Scatter()
Collective Reduce()
Collective Allreduce()
Collective communication: A set of communication patterns that application processes follow to communicate with each other in a parallel computing cluster. These patterns include One-to-Many, Many-to-one, or Many-to-Many delivery mode.

## Slide 3: Factors should be taken into account for CCO
Parallism strategies
  DP, MP, PP, and MoE
Topologies
  High capacity Clos or Dragonfly.
Transport related issues
  Flow control: CBFC, PFC
  Retransmission: go-back-N or selective?
Data Input Method
  Pull: need at least 1-RTT for initialization, high latency but good reliability.
  Push: 0-RTT initialization, low latency but not reliable, need careful design of flow control.
Data Synchronization
  very important for some collective operations, for example, Allreduce, for computation correctness.
Error Recovery
Data parallel | Allreduce
Model parallel | Allreduce & Allgather
Pipeline parallel | Send & Recv
MoE | All-to-All
Notes: 解释清楚 OTT 和 ISP 的出发点不同

## Slide 4: What may be different for inter-DC CCO
Parallism strategies
  should leave bandwidth sensitive operations within single DCs
  need careful scheduling algorithms[1], for example, apply PP and DP on inter-DC traffic
Topologies
  inter-DC doesn’t have high capacity link like intra-DC networking
Transport related issues
  go-back-N retransmission may incur much redundancy and delay over wide area
Data Input Method
  pull method incur much latency over WAN
  should consider hybrid approach or push method with dedicated flow control
Data Synchronization
Error recovery
  design better check point algorithms
[1] Decentralized Training of Foundation Models in Heterogeneous Environments, NeurIPS 2022
Notes: 解释清楚 OTT 和 ISP 的出发点不同

## Slide 5: Potential IETF landscape of CCO
  Design new transport and routing protocols
    RDMA over WAN has some previous work, like iWARP, RoCEv2.
    iWARP is merely used for AI training, because of its performance. RoCEv2 is primarily used within DCs, and it is not maintained in IETF.
    Better congestion control and flow control
    Collective semantic aware routing? switches and routers can be aware of the collective operations or even offloading part of collectives.
*CCL
Application
Verbs/Libfabric
Vendor Implementation of CC
Notes: 解释清楚 OTT 和 ISP 的出发点不同